## Slide 1: Forecast error costs little and does not move prices, so keep selling the forecast
84%
of 2026 half-hours landed inside our 80% forecast interval (95% interval: 94%)
-£0.33
per MWh for each GW of wind shortfall; 95% CI -£1.4 to +£0.6, so no detectable price effect
£265k
imbalance cost for a 1 GW portfolio, Jan-Sep 2026: 0.12% of its revenue
Decisions we need today
1
Keep selling the forecast. Do not shade volumes below it.
2
Hold credit for a bad day: about £0.3m per GW.
3
Approve a data-gap study (gas, imbalance volume, outages, 2024 wind) before any pricing change.
Notes: Open with the answer. We asked whether wind coming in below its day-ahead forecast pushes the imbalance price above the day-ahead price, and what that costs a wind owner. Three numbers: our 80% intervals held up on 2026 (84%); the price slope per GW of shortfall is statistically zero (-£0.33, interval -£1.4 to +£0.6); and forecast error cost a hypothetical 1 GW portfolio £265k in Jan-Sep 2026, 0.12% of revenue. Ask for the three decisions at the end of the discussion, not now. Caveat to state early: public-data associations, hypothetical portfolio.

## Slide 2: The forecast is close to unbiased, even when wind is high
Chart: Mean error by forecast level (% of capacity)
| Q1 lowest | Q2 | Q3 | Q4 | Q5 highest
Mean error, % of capacity | 1.43 | 1.09 | 1.42 | 1.83 | 0.42
Chart: Mean error by hour of day (% of capacity)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Mean error, % of capacity | 1.24 | 1.05 | 1.03 | 1.02 | 0.83 | 0.01 | 0.65 | 0.73 | 0.4 | 0.3 | 0.48 | 1.15 | 1.56 | 1.76 | 1.82 | 2.1 | 1.88 | 2.17 | 2.04 | 1.94 | 1.48 | 1.39 | 1.17 | 1.15
+1.2%
mean error: wind averaged 273 MW above forecast
6.1% | 9.1%
mean absolute | RMS error, as % of capacity
84% | 94%
of 2026 half-hours inside 80% | 95% intervals; autumn only 66%
Positive = wind above forecast. Intervals fitted on 2024-25 and tested on 2026; autumn is September 2026 only.
Notes: The worry was that the day-ahead forecast over-forecasts when wind is high. It does not: the top quintile averages +0.4% of capacity with an interval that includes zero. Bias is small everywhere (+1.2% overall) and a little higher in afternoons. On forecast ranges, the 80% intervals we fit on 2024-25 contained 84% of 2026 half-hours at an average width of about 4.4 GW (18% of capacity). Autumn is the weak spot at 66%, but that is September 2026 only. Earlier in the project we saw a false 14% over-forecast because we had used metered wind as 'actual'; total wind removes it. Likely question: how wide is the band for one GW? Roughly -70 to +120 MW per GW for the middle 80%.

## Slide 3: Wind shortfall does not detectably move imbalance prices
Chart: Raw: mean spread by wind shortfall (GBP/MWh)
| Surplus >1 GW | Within 1 GW | Short 1-2 GW | Short >2 GW
Mean spread, GBP/MWh | -1.1 | 0.97 | 2.27 | 2.26
-£0.33
adjusted slope per GW of shortfall (95% CI -£1.4 to +£0.6), after controlling for demand, MID, hour and month
+0.11
slope on 2026 alone (2024-25: -0.21); adding shortfall does not improve out-of-sample prediction
2.4% vs 2.3%
share of half-hours with a spread above £50: after a >2 GW shortfall vs all periods
+£0.42
slope if the most extreme 1% of spreads are capped; not significant in 2026
The raw rise looks like a wind effect but is not once controls are added. Association only: demand errors and outages also move with wind.
Notes: The left chart is what people expect to see: spreads rise from about -£1 when wind beats forecast to about +£2 when it misses. The right side is why we do not believe that is a wind effect. With controls for demand, MID, hour and month the slope is -£0.33 per GW and the interval comfortably includes zero, in the bootstrap (resampling whole days) and with HAC errors. It is -0.21 on 2024-25 and +0.11 on 2026. Big shortfalls do not raise spike risk (2.4% vs 2.3%). If we cap the most extreme 1% of spreads a small positive slope (+£0.42) appears, but not in 2026. Exploratory splits suggest any effect lives in summer (+£1.14) and low-demand periods; 12 splits, no correction, so a lead only. We say 'moved with', not 'caused'.

## Slide 4: Forecast error costs little on average; the exposure is one bad day
Chart: Cost of selling the forecast (GBP per MWh)
| 2024 (141 days) | 2025 | 2026 (Jan-Sep)
GBP per MWh generated | 0.22 | 0.34 | 0.11
Chart: 2026 saving from selling less than the forecast (%)
| 1st | 10th | 20th | 30th | 50th
Raw spreads | 119 | 42 | 38 | 13 | -17
Extremes capped | -34 | -10 | 8 | 1 | -2
£265k
2026 cost (Jan-Sep): 0.12% of revenue, 0.47% in 2025
£263k
one day, 8 Jan 2025: 21% of that year's cost
£0.36-1.24m
ceiling per GW-year on what a perfect forecast could save
Hypothetical 1 GW portfolio with the national error profile, so real costs will be higher. Selling less only 'saves' by being long when system price runs above MID; it fails once extremes are capped.
Notes: Cost per MWh generated for selling the forecast: £0.22 in 2024 (only 141 usable days), £0.34 in 2025, £0.11 in 2026. In pounds, £265k for Jan-Sep 2026 on a 1 GW portfolio, 0.12% of MID-valued revenue. Errors partly cancel: in 2025 the portfolio lost £5.5m in bad half-hours and gained £4.3m in good ones. The tail is the exposure: 8 Jan 2025 alone cost £263k. The right chart tests selling less than the forecast. The 1st-percentile version looks like a 119% saving in 2026, but that is a bet on system price staying above MID while being long in 99% of periods. Cap extreme spreads and it is -34%; no quantile gives a saving that holds up. The £0.36-1.24m ceiling is the cost of selling the forecast in 2026 (annualised) and 2025: even a perfect forecast could not save more than that per GW-year.

## Slide 5: What we recommend, and what would change our minds
Recommended actions
1
Keep selling the forecast; do not shade below it.
2
Hold credit for a bad day (about £0.3m per GW). Normal range: -70 to +120 MW per GW.
3
Cap forecast-improvement spend well below the £0.36-1.24m per GW-year ceiling.
4
Use the 80% intervals, but assume about 66% coverage in autumn.
5
Close data gaps first: gas, imbalance volume, outages, 2024 wind, real portfolio errors.
We would revisit if
Any adjusted slope interval excludes zero (watch summer, low demand)
Imbalance pricing rules change
Battery build-out changes spreads
A third forecast disagrees with ours (NESO file: +3.6% bias)
Rolling three-month interval coverage leaves the 75-90% range
Know the limits
No gas price. Hypothetical 1 GW portfolio with the national error profile. 229 days of 2024 dropped for faulty source data. No intraday trading or balancing actions. Associations, not causal effects. Re-run each quarter. Sources: Elexon Insights, NESO Data Portal.
Notes: Close with the asks. 1) Keep selling the forecast, no shading. 2) Hold credit for a bad day, about £0.3m per GW. 3) Approve the data-gap study: gas price, net imbalance volume, outages, demand forecast error, total wind for April-November 2024, and the real portfolio's own errors. The right panel is what would change our minds: an interval excluding zero, a pricing rule change, battery growth, or a third forecast that disagrees. Be upfront about limits: no gas price, hypothetical portfolio, a source data fault that removed 229 days of 2024, no intraday or balancing actions. The thresholds here are suggestions, not tested rules. Sources: Elexon Insights (WINDFOR, AGWS, system prices, MID, demand outturn) and the NESO Data Portal.